## Slide 1: Comparing Speech Intelligibility with varying SNR, Reverb
Mezisashe Ojuba
12th June 2024.

## Slide 2: Effect of Noise, Reverb on Cochlear Implants
Previous studies have explored the effects of noise and reverberation on hearing sensation for cochlear implant users.
Sound localization is difficult for people with CIs in reverberant rooms (Kerber et al., 2013).
(Badajoz-Davila et al., 2020) found that In small reverberant rooms, speech intelligibility is more affected. In Noise, SI reduced, but worse in fluctuating than stationary noise.
Notes: Unlike hearing people, Deaf/HoH people with cochlear implants are affected by minute ambient noise and reverberation differently. For example, as Kerber 2013 states, sound localization is difficult for people with CIs in reverberant rooms.
Previous studies …
sers of bilateral cochlear implants (CIs) experience difficulties localizing sounds in reverberant rooms, even in rooms where normal-hearing listeners would hardly notice the reverberation. (https://www.ncbi.nlm.nih.gov/pmc/articles/PMC3642272/#:~:text=Users%20of%20bilateral%20cochlear%20implants,would%20hardly%20notice%20the%20reverberation.)

## Slide 3: Cochlear Implant Simulation with Varying Overlap
I simulated the auditory processing pipeline with 2ms, 3ms, 6ms, and no overlap with 22 channels.
I noticed that the pitch rose the shorter the overlap, resulting in a tinny metallic sound. I was not able to identify the reason for this.
Original Sound: “cosmos”
2ms overlap
4ms overlap
6ms overlap
No overlap
Notes: Before I get into my methods, I would like to briefly mention this.
As such, I used 22 channels (gotten from svirsky) with no overlap

## Slide 4: Method
Normalized sound using Pydub so all signals are the same power
Varied signal to sound ratio
Simulated cochlear implant
Using speech intelligibility metric
Repeat process while varying the level of reverberation
Notes: Was working on speech intelligibility metric yesterday and this morning, not completed

## Slide 5: Sound Demo - Varying Noise
SNRs: 0.25, 0.5, 0.75, 1, 1.25, 1.5, 2, 7, no noise added
No noise
Output (no noise)
0.5 SNR
1.5 SNR
7 SNR
Notes: I used ambient traffic (truck) noise gotten from
For demonstration purposes, I will only show four of the SNRS.
I am yet to implement speech intelligibility metric using a speech intelligibility library i found online.
I also got stuck adding reverb to sound using scipy.signal.convolve, but got stuck for a minute understanding what the parameters mean.

## Slide 6: Other Tasks
Matlab
  Implemented the same code as did in Python with same results
  Looked into real time processing and buffering, but could not progress because bandpassing was extremely slow and introduced an excessive delay.
  Dspcochlear and Signal Processing Library
Electrodogram

## Slide 7: References
Badajoz-Davila J, Buchholz JM, Van-Hoesel R. Effect of noise and reverberation on speech intelligibility for cochlear implant recipients in realistic sound environments. J Acoust Soc Am. 2020 May;147(5):3538. doi: 10.1121/10.0001259. PMID: 32486825.
Kerber, S., & Seeber, B. U. (2013). Localization in reverberation with cochlear implants: predicting performance from basic psychophysical measures. Journal of the Association for Research in Otolaryngology : JARO, 14(3), 379–392. https://doi.org/10.1007/s10162-013-0378-z
Svirsky, M. A., Fitzgerald, M. B., Sagi, E., & Glassman, E. K. (2015). Bilateral cochlear implants with large asymmetries in electrode insertion depth: implications for the study of auditory plasticity. Acta oto-laryngologica, 135(4), 354–363. https://doi.org/10.3109/00016489.2014.1002052
Jupyter Notebook